Version No. 0106

Armourtech DPS 101

Deep penetrating Concrete sealer

# Description:

# Armourtech 101 concrete sealer is a specially formulated high-tech clear/flat water based sealer that “fuses” to concrete and appreciably helps stop water, oil, gas, grease, salts and other  fluids from damaging concrete.

# Armourtech 101 unique formula reacts with the lime in the concrete and directly with the Silica content and hardens and consequently densifies the concrete, decreasing the moisture permeability and porosity. By this fusion, the substrate actually becomes better concrete.

# Armourtech 101 is waterborne contains no VOC’s, is non hazardous non toxic & no odour.

Uses:

New construction or Existing concrete – as deep penetrating sealer

Below grade / pre-cast / tilt-up / form / bridge decks

Driveways / Walkways/ Basements /Concrete Pavers / Split face /Masonry products / Mortar / Pool decking / Stucco / Bridges / Tunnels / Foundations / Parking Garages / Warehouse Floors / Decorative & Coloured Concrete Applications…	any concrete structure or product

Application:

Surface may be a little damp but not wet. Surface/outside temperature should be 1.5 degrees C or more.

Apply by low-pressure spray – a common garden sprayer works	well.  Apply an even blanket mist just to wet – not soak.   When over applied, white, chalky deposits may appear after drying & these can be stiff-broomed or power washed off.

###### New Concrete:  Use as the Cure & the Sealer

###### Ideally, the best time to apply is when bleed water is gone, and concrete will withstand the weight of a man. OK to apply anytime after placement. Avoid rain or freezing for 12 hours. Apply by spray with medium saturation, careful not to over apply. * We recommend a maintenance mist after the 28-45 day curing cycle complete, if possible, for best results.

###### Old Concrete:  Use as a Penetrating Sealer

Always clean, rinse thoroughly, especially when using oil/citrus base cleaners.  Flush out well, let dry and apply by low-pressure	spray. Acid etching may be necessary for tight or smooth troweled surfaces to aid in penetration.

- Always test first for penetration receptibility.

- Armourtech 101 can be trafficked on immediately by light and heavy traffic of any type.

Armourtech Solutions -Seals – Conditions – Protects

www.concretesealers.co.nz

Version No. 0106

Armourtech DPS 101

Deep penetrating Concrete sealer

Finish: 			Flat

Colour:          		Clear

Coverage:		5-10m2 per/ltr

No. Applications:	1 typically- with porous concrete more applications are possible

Drying Time:		3 – 5 hours per application

Shelf Life:  		2 years, stored unopened above freezing temperature

Clean Up:  		soap & water (avoid contact with glass & plastic windows & lenses)

Note: DO NOT FREEZE

Preparation:

Surfaces must be clean and free of dirt/debris/mildew/oils/grease/curing compounds and other sealers. Seal all cracks prior to use of Armourtech DPS101.

For tight smooth troweled surfaces to aid penetration of Armourtech DPS 101 acid etching or grinding/sanding may be necessary.

Should concrete require acid etching (hydrochloric acid) ensure the concrete is neutralised Sodium Bicarbonate (baking soda) after etching. Dissolve qty baking soda with water (1kg/20ltrs water) allow to settle and drain of the liquid. Spray liquid on concrete and wash out with copious amounts of water. Alternatively a concrete grinder may be required.

Armourtech 101 will not work with any other product with an oil base, such as asphalt, paints, vinyl, etc.  When Armourtech 101 cannot penetrate or over applied, a slight chalky residue may lay on surface. A stiff broom, power cleaning or time will remove this.

Armourtech 101 is not designed to seal cracks and these should be addressed before sealing with Armourtech DPS101.

Clean up:

Clean up spray equipment with soapy warm water.

Health & Safety:

Avoid contact with skin & eyes.  EPA/OSHA Compliant – contains no solvents/0% VOC (Volatile Organic Compounds). Non-Hazardous to plants and animals. Wash application materials 	with water.

First Aid:

Eyes:  Flush with water for at least 15 minutes.  Wash skin thoroughly with soap and water.

If swallowed, give 2 glasses of water to drink & consult physician.

Armourtech Solutions -Seals – Conditions – Protects

Version No. 0106

Armourtech DPS 101

Deep penetrating Concrete sealer

Boiling Point:                  212 F (same as water)

Vapour Pressure:              /20C/68 F water

Vapour Density:                N/A

Solubility in Water:          Excellent

Evaporation Rate:          Same as water

Appearance & Odour:    Clear-slightly amine

Specific Gravity:             (H20-1):1.1 to 1.3 @ 20C

% Volatile by Volume:    N/A

PH:                                 11.5

Flashpoint:                      N/A

Flammable Limits:           N/A

ASTMD 2939:    	Resistance to water solubility, flexibility, no cracking.

ASTMD 466:     		Resistance to water flow and Action. Excellent adhesion. No 					demulsification.

ASTME 96:        	Water vapour transmission 0.04 grains/sq ft./hr.  Water permeability–				0102 perms

ASTMC 836:    		Film thickness on a vertical scale

SS-W-110C:      	Water repellence on masonry test: 1.925% avg.

ASTMC672:       	Freeze/thaw cycle – 100 day cycle

ASTMC-156:     		Water retention 0.47 kg/m2, Specification – 0.55 kg/m2

ASTM C309-98a: 	Moisture loss – 1025 kg/ms

ASTM C115-00: 	Moisture loss – 0.19 kg/m2

Adhesion ASTM: 	Elcometer Pull – 280 lbs-concrete failed 1st / no delaminating

ASTM C642 & C672 	Absorption:  Phase 1-48 hr: 0.64%;  Phase 2-50 day: 1.32%

ASTM Sealing Resistance:  No Scaling

This product is considered a non-hazardous chemical under the OSHA Hazard Communication Standard / (29CFR 1910.1200)

Armourtech Solutions -Seals – Conditions – Protects

www.concretesealers.co.nz